ORIGINAL OPERATING INSTRUCTIONS

Read carefully and retain for future reference

Ceramic Heater

Type: RFC

Models: RFC500; RFC1000; RFC1500; RFC 2000

IMPORTANT WARNINGS

Dear Customer:

Thank you for your confidence in us by purchasing this radiator. These appliances are extremely safe, silent and easy to install.

They do not require special maintenance. They are made of extruded aluminum, a material of high durability respectful to the environment. Before starting it for the first time, carefully read these instructions. Retain them for future references.

GENERAL SAFETY INSTRUCTIONS

1.	Please read carefully these instructions before starting the device for the first time.Keep these instructions, as well as the guarantee, your invoice and if possible, the complete packing with all the elements inside.

2.	The guarantee will cease to be valid in the case of not following the recommendations of this manual.

3.	Before connecting the appliance, make sure the mains voltage is the 230 Volts, and correspond to the marked on the nameplate of the appliance.

4.	Check that the power is sufficient to supply the appliances. The total draw of the radiators' currents must not exceed the capacity of the circuit breaker that protects them.

5.	This radiator cannot be used in rooms with presence of gases or other flammable products (glues, etc...).

6.	WARNING: To prevent overheating, do not cover the device. Do not use the device to dry clothes.

7.	Make sure the power cable or other objects do not come into contact with the radiator surface while in operation.

8.	If the power cable becomes damaged it must be replaced by the manufacturer or a suitably qualified trades person. Failure to comply may danger your safety and voids your warranty.

9.	Check the device and the supply cord regularly. Do not turn the device on if it is damaged.

10.	PRECAUTION: Some parts of this product can reach very high temperatures and cause burns. Pay special attention when children or vulnerable people are around.

11.	Do not place the device straight under a power socket.

12.	Children under the age of three should not be allowed to touch or play with the radiator and should be supervised at all times.

13.	This device can be used by children under 8 years of age, as well as by people with reduced physical, sensory or mental capabilities when suitably supervised and only when they have been provided the instructions regarding the use of the device and have understood the risks that could derive from it. Cleaning  must only be carried out by an appropriate adult.

14.	Children between3 and 8 years should not turn on or off the device, unless this is installed or placed in a normal position and that children are under proper supervision or have received instructions regarding the use of the device as security and they have perfectly understood the potential dangers. Children between 3 and 8 years old should not connect, adjust or clean the appliance or perform any maintenance measure.

15.	Warning: Do not use this heater near baths, showers or swimming pools. It should not be possible to access the device's controls from the bath, shower or any other surface that is in contact with water.(Its use in zones 0 or 1 in bathrooms is totally prohibited: seek advice from a qualified electrician).

16.	For greater safety, this appliance is provided with a device that interrupts its operation in the case of overheating.

17.	This radiator has been designed exclusively to be fixed to the wall. For further information on the fixing systems, consult the section "INSTALLATION ANDWALL MOUNTING" of this manual.

18.	Do not use accessories that have not been recommended by the manufacturer, as they could entail a potential risk to the user, and damage the device. Use only original accessories.

19.	Keep all the packaging elements (plastic bags, cardboard and polyethylene)out of the reach of children, as they can cause potentially dangerous situations.

20.	Use this device only for domestic / light commercial use and the tasks for which it has been designed. This device has not been designed for industrial use. It must not be used outdoors, in greenhouses or for animal husbandry. Keep it away from heat, direct sunlight, humidity and cutting tools. Do not under any circumstances immerse in water or use this device with wet hands. In the case of humidity or water in the device, immediately disconnect the power supply and do not touch the wet parts.

21.	Do not attempt to service the device yourself. Contact a qualified technician.

22.	To disconnect the transmitter from the mains pull the plug, never of the supply cord.

23.	Respect the "SPECIFIC SAFETY INSTRUCTIONS FOR THIS APPLIANCE" listed below

SPECIFIC SAFETY INSTRUCTIONS FOR THIS DEVICE

- The appliance must remain in a vertical position.

- Make sure the appliance is secured at all times. Please adhere to the installation distances indicated in this guide.

- Do not hang any object in front or on top of the device.

- Always ensure that the inlet and outlet air are not obstructed.

- Always install the device so that it cannot enter into contact with any combustible material such as curtains or towels (take into account the gusts of wind).

- To clean the device, consult the instructions in the "MAINTENANCE" section, because if water enters the air grilles it could seriously damage the device.

- Do not insert any object through the grille or inside the device.

- This radiator is designed to be connected by plug to the electric installation and fixed to the wall installation. Follow the instructions in "INSTALLATION".

- The guarantee will not apply if these instructions have not been observed.

INSTALLATION

- During the first use and for a few minutes, could occur smells and noise due to the dilatation of some internal parts. This is normal, so you must provide adequate ventilation. The smells are momentary and quickly will dissipate.

- For greater efficiency, make sure to calculate the power or the number of elements of the apparatus according to the surface of the room. We recommend contacting your dealer performing this calculation.

- Fix the radiator to a firm wall and make sure it is well-levelled, in a room with no furniture and no objects avoiding around.

- Avoid installing the appliance in corners.

- We advise against installing the appliance under the windows, because it is favoring the heat loss.

- The radiator must be away, at a minimum distance of 15 cm from any combustible material, curtains, furniture, chairs, etc.(Fig. 1).

- Allow for a minimum distance of 1 m, from the front of the unit to any obstacles (furniture, walls, curtains, for example) that could hinder its operation.

- Also keep a minimum distance of 15 cm between the appliance and the side walls and any other obstacles (walls, for example) that may affect its function. Also keep a minimum distance of 35 cm on top the appliance free of obstacles and a minimum distance of 15 cm from the floor.

- WARNING: If this appliance is installed in a bathroom, it must be installed only within Zones 2 or Outside Zones (Zone3), according BS 7671 Requirements for Electrical Installations, Section 701. The installation of this appliance within Zones 0 or 1 of a bathroom is totally prohibited. The figure 2 bellow is only for information purposes, we suggest you contact a professional electrician.

| - Minimum Distances - Fig.1 | Zone 1: Appliances supplied to Safety Extra Low Voltage (SELV). Zone 2: Electrical Appliances Class II – IP X4 Zone 3: Electrical Appliances protected by RCD 30mA Fig.2 |
| --- | --- |

WALL-MOUNTING

The appliance is equipped with the following:

- 2 radiator's suspension supports.

Secure the appliance to the wall, you should use the template attached to the box. Follow these instructions:

1. Place the template on the floor and against the wall where you will place the radiator.

2. Mark on the wall the location of the four holes.

3. Drill four holes for inserting the 8 mm plugs.

4. Fix the supports (as shown in the Figure) using the 4 screws and 8 mm plugs .

5. Hang the radiator in the supports fixed on the wall and, finally , completely screw up the two security pieces of the supports.

ELECTRIC SUPPLY CONNECTION

This appliance is equipped with a supply cord H05V2V2-F 2x1.0mm² and bipolar plug without earthing.

Connect the plug to the base outlet.

Check the condition of your electrical installation and connection cables.

This appliance doesn't require earthing connection, due it has double electrical insulation.

Contact a licensed electrician for assistance.

TECHNICAL CHARACTERISTICS

| Brand |  |
| --- | --- |
| Model | RFC |
| Type | RFC500 | RFC1000 | RFC1500 | RFC2000 |
| Rated Voltage | 230 V~ | 230 V~ | 230 V~ | 230 V~ |
| Rated Frequency | 50 Hz | 50 Hz | 50 Hz | 50 Hz |
| Rated Power Input | 500 W | 1000 W | 1500 W | 2000 W |
| Electrical Protection Class | II | II | II | II |
| IP Protection Degree | IP24 | IP24 | IP24 | IP24 |
| Dimensions (LxHxD) (mm) | 380x585x105 | 510x585x105 | 640x585x105 | 770x585x105 |
| Weight (kg) | 5,7 | 8,7 | 11,50 | 14,8 |

DIGITAL PROGRAMMABLE THERMOSTAT

The radiator is equipped with a digital, programmable thermostat.

- User interface

- Display

- 1: Operating mode menu (active mode is framed)

- 2: Program number or parameters number if “3” is displayed

- 3: Installation parameter menu

- 4: Key lock function indicator

- 5: Room temperature indicator

- 6: Type of time (12H AM/PM or 24H)

- 7: Temperature unit

- 8: Heating demand

- 9: Display zone for time, temperatures and parameters

- 10: Graphic view for the current day program

- 11: Current day of the week or Eco design information (comfort mode)

- 12: Pictogram for pilot wire indication or for edit program mode or for consumption power menu

- 13: Overrid function in AUTO mode or ITCS function if blinking

- 14: Opened window detection

- Keyboard

Keyboard is composed by 5 buttons:

- : On/Off key

- : minus key

- : validation key

- : plus key

- : right navigation key

- First installation

During the first installation of thermostat or when a product reset has been done, user has to set the hour and the date (see paragraph II.4.g).

Menu for mode selection

To change the current mode of the thermostat, the user has to push the right navigation key  to display the working mode line.

User moves the frame cursor to choose a working mode. In order to select choosen mode, user pressesor  or . If user doesn’t validate choosen mode, thermostat returns automatically to the older selected mode.

With touch  , user acceds directly to Off mode :

If there isn’t any validation, thermostat returns to an old selected mode: , ,  or .

Parameter menu is available by pressing and maintaining  during 5 seconds (see paragraph parameter menu).

Working mode definition

- Comfort mode

|  | In this mode, comfort temperature set point will be followed all the time. From the screensaver (lighted backlight), by pressing and keys, the comfort setting temperature starts to blink and can be modified. By pressing key, the set point value is validated. If user doesn’t validate the new setting, it will be validated automatically after few seconds. This set point will be used in AUTO mode during high step of selected program . From the screensaver, key permits to switch displaying between measured temperature and setting temperature. By pressing key, thermostat is turned off. By pressing key, navigation menu is displayed. Default Value: 21 °C Range: 5.0°C to 30°C |
| --- | --- |

- Reduced mode

|  | In this mode, the reduced set point temperature will be followed all the time. From the screensaver (lighted backlight), by pressing and keys, the reduced setting temperature starts to blink and can be modified. By pressing key, the set point value is validated. If user doesn’t validate the new setting, it will be validated automatically after few seconds. This set point will be used in AUTO mode during low step of selected program . From the screensaver, key permits to switch displaying between measured temperature and setting temperature. By pressing key, navigation menu is displayed. By pressing key, thermostat is turned off. Default Value: 19 °C Range: 5.0°C to 19°C |
| --- | --- |

- Automatic mode

|  | In this mode, the thermostat will follow the chosen program (Built-in P1 to P9 or customized U1 to U4) according to the actual time and the Comfort and Reduced setting temperature. From the screensaver, key permits to switch displaying between measured temperature, setting temperature and time. From any screen, by pressing and keys, user can override, until next program step, the current program temperature by changing the value. The value starts to blink and can be modified. By pressing key, the set point value is validated. The small hand logo will be displayed when override function is active. This override will continue until the next step (program switch to another temperature setpoint) or during 2H maximum. By pressing key, navigation menu is displayed. By pressing key, thermostat is turned off. |
| --- | --- |

- Anti-freeze mode

|  | In this mode, anti-freeze temperature set point will be followed all the time. The anti-freeze setting temperature is fixed. However, it can be adjusted in the parameter menu ‘AF’ (see chapter 6). The default value is equal to 5°C. From the screensaver (lighted backlight), , and keys permit to switch displaying between measured temperature and setting temperature. By pressing key, navigation menu is displayed. |
| --- | --- |

- OFF Mode

|  | In standby mode, only OFF mode logo is displayed. After pressing one of 4 keys (or or or), measured temperature is displayed. Another pressing permits to display the time. After few seconds, these informations aren’t displayed. If the touch is pressing, thermostat will wake up in the last selected mode. |
| --- | --- |

- Timer/boost mode

|  | This mode allows the users to adjust the setpoint temperature during choosen duration. Time setting: pressing permits to set the time value with and . Touch permits to validate time value and to switch to the setting of setpoint temperature. Default value: 0 Value range: 15, 30 or 45 minutes or 1 to 23 houres or 1 à 44 days Setpoint temperature setting: Pressing on touch or permits to set set point temperature.Touch permits to validate the value and to activate boost period. Default value: 24°C Value range: 5.0°C à 37°C Timer is running: the boost logo is flashing and values of setpoint and remaining time are displaying alternatively. Pressing permits to display measured temperature. Pressing or permits to change settings. Pressing stops timer. Pressing stops product and clear timer counter. Timer end: The thermostat returns to the old selected mode. |
| --- | --- |

- “Edit time” menu

|  | Time displaying: After the selection of this mode, pressing the keys or or starts time and date settings. Pressing key returns to the mode selection menu. Time and day settings: - Adjustment of the hours - Adjustment of the minutes - Adjustment of the day (1 corresponds to Monday). Date settings: - Adjustment of the Month (01 corresponds to January) - Adjustment of the day number - Adjustment of the year. Each time that a value is blinking, it can be adjusted with and keys. The setting value is validated with or keys. If there isn’t any touch pressing, thermostat returns automatically to the old selected mode. Modifications will be saved automatically. Pressing stops product and clears edited values if there aren’t be validated at the end of date setting. |
| --- | --- |

- Program menu

|  | Current program displaying: Pressing permits to change the day for program displaying. Pressing returns to auto mode. Pressing or permits to edit the program number. Program number editing: Pressing permits to change the day for program displaying. Pressing or permits to change the program number. Pressing permits to validate selected program. Pressing one second when a User program is selected permits to edit it. Built-in program: P1 to P9 described paragraph “Built-in program description” User program editing: Pressing permits to change interval time. Pressing activates a reduced temperature at the current interval time. Pressing activates a comfort temperature at the current interval time. Pressing validates the edited day. If the seventh day is validated, thermostat returns to Auto mode (see paragraphe “User program editing”). Default: Reduced set point temperature every day Pressing stops product and clear program selection and program edition if the last day wasn’t validated. |
| --- | --- |

- Power consumption menu

|  | This mode is only available if a heater power has been setted by user. Pressing or permits to change interval time for power consumption displaying (last 1 hour, last 24 hours, last 7 days and last 30 days). The power values are displaying with kWatt unit. If there isn’t any touch pressing, thermostat returns automatically to the old selected mode. Pressing permits to return in selection mode menu. Pressing one second resets power consumption values. Pressing stops product. Estimated values are saved in EEPROM memory every 4 hours and each time user displays this menu. If there is powercut, estimated values are kept during 12 hours after there are resetted. |
| --- | --- |

Built-in program description

P1: 	Morning (7h-9h), Evening (17h-23h) & Week-end (8h-23h)

P2: 	Morning (7h-9h), Afternoon (12h-14h), Evening (18h-23h) & Week-end (8h-23h)

P3: 	Week (6h-23h), Saturday (7h-24h) & Sunday (night (0h-1h), day (7h-23h))

P4: 	Evening (15h-23h) & Saturday (7h-24h) & Sunday (night(0h-1h), day(7h-23h))

P5: 	Morning (6h-8h), Evening (21h-23h) & Saturday (Morning (6h-8h), Evening (18h-24h)) & Sunday (Morning (6h-8h), Evening (18h-23h))

P6: 	Morning (6h-8h), Afternoon (14h-21h) & Week-end (7h-21h)

P7: 	Office: Monday to Friday (7h-19h) & Week-End (stop)

P8: 	Shop: Monday to Friday (8h-19h) & Saturday (8h-18h) & Sunday (stop)

P9: 	Sacond home: Friday (13h) to Monday (7h)

User program editing

When a user program is editing, thermostat displays:

Temperature pictogram:

- : comfort temperature is applied during selected time interval

- : reduced temperature is applied during selected time interval

Time interval:

- Step of 30 minutes

Edition description:

- Program edition starts with the first day of the week (1=monday)

- Pressing  key activates a reduced temperature () at the cursor position

- Pressing  key activates a comfort temperature () at the cursor position

- Pressing key moves cursor to the right

- Pressing key validates the edited day. Next day will keep same settings as previous edited day in order to help user edition. When the seventh day is validated, thermostat automatically returns to the Auto mode.

EEPROM saving settings

This thermostat saves its data (setpoint values, user program and settings) automatically when:

- User validates setting modifications by pressing validation key ;

- Product backlight turns off.

It saves too estimated values of its power consumption:

- Every 4 hours;

- When user goes in consumtion mode.

Special functions

- ITCS: Intelligent Temperature Control System

This function can be activated with the “ITCS parameter” in menu parameter (see chapter “parameter menu”).

This function permits to activate your installation in advance (2 hours maximum) when your thermostat is in Auto mode . This function assures the desired temperature at the hour programmed following your weekly program.

To operate, this ITCS realizes automatically several time and temperature measurements. The goal is to estimate a heating speed of the system. With this value, system can calculate the time to activate the heating in advance.

When thermostat is switched on for the first time, a default time is used to reach the setting temperature. This value will be adjusted by new measurements at each program change to offset the outside temperature evolution. Then, the thermostat can be programmed without adjustment because it will be done automatically.

When an adaptative start is realizing by the system, a hand logo  is displayed on LCD screen.

- Opened windows detection

This function can be activated with the “window parameter” in menu parameter (see chapter “parameter menu”). If the function is activated, the icon  will appear on the screen:

This function is done by measuring and recording the temperature evolution within the last 30 minutes:

- First step - Windows open triggered: The remote goes in windows open status ( and temperature value blink) when, during last 30 minutes, the temperature as decreased of more than 1.5°C

- Second step: During 30 minutes, if temperature rises than 0.3°C then window open status is cleared and remote automatically comes back to current mode set point.

- Time saving

This product can keep time counting during 12 hours after a power outage. Beyond 12 hours without power, hour displaying will blink until user goes to edit time menu in order to check time anfd date values:

If power outage is too long, time and date values will be reseted with factory value. User will have to reconfigure these values.

- Keyboard locks

To activate this function, the user maintains pressing  key and then presses simultaneously on  key.

This function can be accessed in any operating mode except in parameter menu (see chapter « Parameter Menu »), in edit time menu, edit program menu and power consumption menu (see chapter « working mode definition ») and in menu for mode selection.

The icon  will be displayed on the screen:

To unlock key board, the user will have to repaet the same procedure.

NOTE: If there is a power loss, the configuration is kept.

Parameter menu

The thermostat has to be in one of those functioning modes: comfort , reduced , anti-freeze , Auto  or timer . To enter in the parameter menu, the user has to maintain during 5 seconds.

The parameter, which will be adjusted, is selected by pressing,  or. The parameter setting is done by pressing   or   keys. The validation of the setted value is done by pressing  key.

Number of parameter menu is changed with  navigation touch.

To leave the parameter menu, the user has to choose “End” parameter and press   key.

|  | Type of degrees displayed “dEG” |
| --- | --- |
|  | Default value | Other choices |
|  | °C (Celsius) | °F (Fahrenheit) |
|  | Selecting the clock display format “time”: 24H → 24:00 12H → 12:00 AM/PM |
|  | Default value | Other choices |
|  | 24H | 12H |
|  | DST – Daylight summer time If this function is activated, thermostat change automatically time (summer/winter) according to date. |
|  | Default value | Other choices |
|  | Yes (activated function) | No |
|  | Calibration of temperature sensor: First screen displays measured temperature. Pressing key displays offset value. If « no » is displayed, sensor calibration hasn’t been done (offset value equal to zero). Setting temperature offset: Pressing or key sets temperature value. Pressing validates setting. How to calibrate temperature sensor: The calibration must be done after 1 day working with the same setting temperature in accordance with the following description: Put a thermometer in the room at the same distance from the floor like the thermostat. Check the real temperature in the room after 1 hour. Enter this value in the calibration parameter menu by using the or keys in order to enter the real value. Press to validate the calibration. User can reset offset value by pressing and during one second. |
|  | Default value | Value range |
|  | No (null offset value) | -5°C to 5°C |
|  | AF – Antifreeze set point temperature Pressing or key permits to configure set point temperature value for antifreeze mode. Pressing validate the setting. |
|  | Default value | Value range |
|  | 5°C | 5 to 10°C |
|  | ITCS – Intelligent Temperature Control System (adaptive start heating in AUTO mode) This function is described in the paragraphe II.8 “Special functions”. This parameter permits to activate or not this functionality. |
|  | Default value | Other choices |
|  | Yes (activated function) | No |
|  | Automatic open window detection This function is described in the paragraphe II.8 “Special functions”. This parameter permits to activate or not this functionality. |
|  | Default value | Other choices |
|  | Yes (activated function) | No |
|  | Setting heater power for calculation of consumption power This parameter corresponds to the heater power. This parameter has to be configured in order to calculate power consumption and to select adapted regulation parameters. |
|  | Default value | Other choices |
|  | 1000 W | 1500 W /2000 W Displaying value are, due to digit number: 1000/1500/2000 |
|  | CLr – clear product memory with factory settings All thermostat parameters will be loaded with factory settings. By pressing and maintaining key during 5 seconds, thermostat resets parameters. Thermostat will be reset with the factory default setting: Set point temperatures 21°C , 19°C , 5°C , program U1 to U4, boost 30 minutes , user parameters: time displaying “24H”, temperature unity “°C”, open window detection “Yes”, ITCS (adaptive start time for heating) “Yes”, sensor calibration “no”, automatic daylight saving time adjustment “Yes”, Reset the time. NOTE: Setting of radiator power isn’t reset. |
|  | Software version |
|  | Exit parameter menu: Pressing key permits to exit parameter menu and return to normal functionning. |

Measurement error

If the sensor is out of order or disconnected, an error message is displayed on thermostat screen.

| Problem on sensor |  | The message « Err » and the logoblink. |
| --- | --- | --- |

THERMAL SAFETY

In the case of overheating, a safety device automatically cuts the radiators operation. After cooling the radiator will automatically reset.

MAINTENANCE

Your radiator requires no regular maintenance, however, to ensure its good operation:

Always disconnect the device from the mains before performing any cleaning or maintenance operation.

Let it cool down before cleaning.

To avoid any risk of electrical shock, clean the unit with a soft, damp cloth to wipe the outside of the radiator and remove dust and dirt cloth.

Do not use detergent, solvent, abrasive products or any other chemical product to clean the radiator.

NEVER immerse the device in water or any other liquids.

You can use a vacuum or flexible brush to clean the air grilles. This maintenance must be carried out regularly to ensure optimum performance. Ensure the radiator is totally dry before turning it back on.

| EU Declaration of Conformity |  |
| --- | --- |

| Product: | Ceramic Heater |
| --- | --- |
| Trademark: |  |
| Models: | RFC500; RFC1000; RFC1500 & RFC2000 |
| Batch & Serial No.: | Mx- YYDDD-XXX (1) |
| (1) Explanation of code "Batch & Serial No.": Batch = Mx - YYDDD; where: Mx = Production Line No.; YY = year and DDD = correlative day (001,..., 365). Serial No.= XXX (001,..., 999). |

We:

HERMANOS JULIÁN M., S.L.

Head Office: Esposos Curie,44 / Factory: Gutenberg,91-93

Polígono Industrial “Los Villares” . 37184 Villares de la Reina . Salamanca . España

Tf.+34 923 222 277  +34 923 222 282 . Fax +34 923 223 397

http://www.hjm.es

Hereby declare that the following equipment complies with all the essential requirements for health and safety of European Directives.

2014/30/EC   EMC DIRECTIVE    2014/35/EC   LV DIRECTIVE

2011/65/UE  RoHS DIRECTIVE    2009/125/EC (ErP Directive)

With reference to the application of the following standards:

| 2014/30/EC EMC DIRECTIVE | EN 55014-1:2006 +A1:2009 +A2:2011 EN 61000-3-2:2014 EN 61000-3-3:2013 EN 55014-2:1997 +AC: 1997 +A1:2001 +A2:2008 EN 61000-4-2:2009 EN 61000-4-3:2006 +A1:2008 +A2:2010 EN 61000-4-4:2012 EN 61000-4-5:2006 EN 61000-4-6:2013 EN 61000-4-11:2004 |
| --- | --- |
| 2014/35/EC LV DIRECTIVE | EN 60335-2-30:2009 + CORR:2010 +A11:2012 EN 60335-1:2012 +AC:2014 +A11:2014 EN 62233:2008 +CORR:2008 |
| 2011/65/UE RoHS DIRECTIVE | EN 62321-1:2013 |
| 2009/125/EC (ErP Directive) | UE 2015/1188 |

| Model: RFC |
| --- |
| Item | Symbol | Value | Unit |  | Item | Unit |
| Heat output 2000 |  | Type of heat output/room temperature control (select one) |
| Nominal heat output | Pnom | 2 | kW |  | single stage heat output and no room temperature control | NO |
| Maximum continuous heat output | Pmax,c | 2 | kW |  | Two or more manual stages, no room temperature control | NO |
| Auxiliary electricity consumption |  |  |  |  | with mechanic thermostat room temperature control | NO |
| At nominal heat output | elmax | 2 | kW |  | with electronic room temperature control | NO |
| In standby mode | elSB | 0.0005 | kW |  | electronic room temperature control plus day timer | NO |
|  |  |  |  |  | electronic room temperature control plus week timer | YES |
| Heat output 1500 |  | Other control options (multiple selections possible) |
| Nominal heat output | Pnom | 1.5 | kW |  | room temperature control, with presence detection | NO |
| Maximum continuous heat output | Pmax,c | 1.5 | kW |  | room temperature control, with open window detection | YES |
| Auxiliary electricity consumption |  |  |  |  | with distance control option | NO |
| At nominal heat output | elmax | 1.5 | kW |  | with adaptive start control | YES |
| In standby mode | elSB | 0.0005 | kW |  | with working time limitation | YES |
| Heat output 1000 |  | with black bulb sensor | NO |
| Nominal heat output | Pnom | 1 | kW |  |  |  |
| Maximum continuous heat output | Pmax,c | 1 | kW |  |  |  |
| Auxiliary electricity consumption |  |  |  |  |  |  |
| At nominal heat output | elmax | 1 | kW |  |  |  |
| In standby mode | elSB | 0.0005 | kW |  |  |  |
| Heat output 500 |  |  |  |
| Nominal heat output | Pnom | 0.5 | kW |  |  |  |
| Maximum continuous heat output | Pmax,c | 0.5 | kW |  |  |  |
| Auxiliary electricity consumption |  |  |  |  |  |  |
| At nominal heat output | elmax | 0.5 | kW |  |  |  |
| In standby mode | elSB | 0.0005 | kW |  |  |  |
| Contact details | HERMANOS JULIÁN M., S.L. Head Office: Esposos Curie,44 / Factory: Gutenberg,91-93 Polígono Industrial “Los Villares” . 37184 Villares de la Reina . Salamanca . España Tf.+34 923 222 277 +34 923 222 282 . Fax +34 923 223 397 http://www.hjm.es |

Requirements regarding ecodesign for local heating:

S = S,on - 10% + F(1) + F(2) + F(3) - F(4) - F(5)

= 40 -10%+0+7+2-0-0 = 39%

RECYCLING (Disposal of the product at the end of its useful life)

According to European Directive 2012/19/UE, on waste electrical and electronic equipment (WEEE), old electrical household appliances cannot be disposed of in the usual municipal containers; they have to be collected separately to optimise the recycling of the components and materials that comprise it, and reduce the impact on human health and the environment.

The crossed-out wheeled bin is marked on all Electrical and Electronic products, to remind the consumer of their obligation dispose of them separately.

The consumer must contact the local authority or the vendor to learn about the correct disposal of his/her old electrical household appliance.

Made by

HERMANOS JULIAN M., S.L.

Factory: Gutenberg,91-93

Polígono Industrial “Los Villares”

ES-37184 Villares de la Reina . Salamanca . Spain

+34 923 222 277 - +34 923 222 282

Fax: +34 923 223 397

Web: www.hjm.es

ESB-37295664